## Slide 1: INTRODUCTION
DNA manipulation in the classroom
2 June 2026

## Slide 2
Objectives
By the end of this course you will:
Feel confident preparing for labs 1, 2, 3 & 5
Feel confident carrying out labs 1, 2, 3 & 5
Be aware of Health and Safety requirements
Know where to access resources
Know who to contact for support

## Slide 3
A sense of scale:
1 litre = 1000 ml
500 ml
500 l
5 ml = 1.tsp
1 ml = 1000 l
1 l is 1 millionth of a litre (1000 ml in 1 litre / 1000 l in 1ml – 1000 x 1000)
20 / 10 / 5 / 2 l

## Slide 4
Lab 1: micropipetting
1 Twist dial to desired volume
2 Add disposable pipette tip
3 Press plunger to first stop
4 Insert pipette tip into solution to be
transferred
5 Slowly release plunger to retrieve liquid
6 Move pipette tip into desired tube
7 Press plunger past first stop to second stop
to transfer liquid, keep the plunger down
as you remove it from the tube.
8 Eject tip

## Slide 5
Lab 1: micropipetting
2 l
5 l
10 l
20 l

## Slide 6
Lab 1: micropipetting

## Slide 7
Lab 1: micropipetting

## Slide 8
Lab 1: micropipetting
1 Twist dial to desired volume
2 Add disposable pipette tip
3 Press plunger to first stop
4 Insert pipette tip into solution to be
transferred
5 Slowly release plunger to retrieve liquid
6 Move pipette tip into desired tube
7 Press plunger past first stop to second stop
to transfer liquid, keep the plunger down
as you remove it from the tube.
8 Eject tip

## Slide 10
Working with Plasmids
Image taken from Wikimedia Commons
Plasmids 101: What is a plasmid? (addgene.org)

## Slide 11
Lab 2: restriction digestion

## Slide 12
Lab 2: restriction digestion

## Slide 13
Lab 2: restriction digestion
3
1
2

## Slide 14
Lab 2: restriction digestion
HindIII
Haemophilus influenza
BamHI
Bacillus amyloliquefaciens

## Slide 15
Lab 2: restriction digestion
pBAD
rfp

## Slide 16
Lab 2: restriction digestion
pKAN-R
pARA

## Slide 17
Lab 2: restriction digestion

## Slide 19
Lab 5: preparation
400 ml 1 x TAE buffer from 50 x concentrate
0.8% agarose gel, 11 ml per gel (make bulk)
With the Mini-One gel system, DNA stain added with LD

## Slide 20
Lab 5: TAE buffer
C1V1 = C2V2
C1= desired concentration
V1= desired volume
C2= stock solution concentration
V2 = volume required

## Slide 21
Lab 5: agarose gel

## Slide 22
Lab 5: Ligation
But first – HEAT INACTIVATION .. 70 C for 20 min
DNA ligation is the joining of 2 DNA molecules by the enzyme, DNA ligase.
DNA ligase catalyzes the formation of two covalent phosphodiester bonds between the 3’ hydroxyl group of one nucleotides and the 5’ phosphate group of another in an ATP dependent reaction.
In molecular cloning the ligation reaction follows the digestion of the gene insert and the target vector.

## Slide 23
pBAD
rfp
Lab 2: restriction digestion

## Slide 24
Lab 2: restriction digestion
pKAN-R
pARA
4,495 bp
377 bp
4,705 bp
807 bp

## Slide 25
Lab 3: Ligation
G
G
A
C
C
T
T
T
C
G
A
A
sticky end
BamH I
sticky end
Hind III
3’
5’
5’
3’
3’
3’
5’
5’
5’
5’
3’
3’
G
C
C
A
T
G
C
T
A
G
T
A
sticky end
BamH I
sticky end
Hind III

## Slide 26
Lab 3: Ligation

## Slide 27
Lab 3: Ligation

## Slide 28
Collect K+ and A+ from 70 C water-bath
Place on ICE. Wait 5 min
Locate LIG tube containing 2.5 l Ligase enzyme
Add 4 l Lig Buffer (LB) and 2.0 l H20 to LIG tube
Add 6 l K+ and 6 l A+ to LIG tube
This tube now contains 20.5 l
This tube stays on the bench, at room temp, o/n for the reaction to happen
Lab 3: Ligation (page 3.3)

## Slide 30
Lab 5: Gel Electrophoresis

## Slide 31
Lab 5: gel electrophoresis

## Slide 32
Lab 5: gel red staining

## Slide 33
Electrophoresis – 2 ways
Tanks & transilluminator (TT)
Mini-One (MO)

## Slide 34
Lab 5: gel tank assembly

## Slide 35
Lab 5: Mini-One assembly

## Slide 36
Electrophoresis – 2 ways
Tanks & transilluminator (TT)
Mini-One (MO)
0.8% gel, 1 x TAE buffer
30-35 ml agarose for each gel
200-300 ml buffer needed
8 or 15 teeth (samples) per gel
Add LD to samples
LD – regular
Load / black card below tank
Run time: 30-45 min
Post-stain: 30 min / Gel Red
Download gel images and share results
0.8% gel, 1 x TAE buffer
11 ml agarose for each gel
135 ml buffer needed
6 or 9 teeth (samples) per gel
Add LD to samples
Ensure LD contains Gel Green
Load under blue light
Run ‘live’ : 20-30 min
No post-stain required
Result recorded directly by students on smartphone

## Slide 37
Before Loading
Remove the masking tape from the ends of your gel tray
Place the gel, and its casting tray, into the electrophoresis tank. The wells should be at the black (negative end), as DNA is negatively charged and will run towards the red (positive) end.
Make sure that the open end of the wells is facing upwards to receive the samples
Submerge the gel in 1X TAE buffer (this contains the ions needed for electrophoresis). There needs to be 1-2 mm of buffer over the top of the gel. Too much and the current will go through the buffer and not the gel! Pour buffer onto the gel until just after the well dimples disappear.
Remove the comb from your agarose gel by lifting it directly upwards. The comb will create some suction, so it needs a gentle, but consistent upwards pressure.
Place a black sheet under the wells to make them more visible
Remove the comb from your agarose gel by lifting it directly upwards.
Place the gel, and its casting tray into the electrophoresis tank (only fits one way!). Remember the black supporting platform and make sure the wells are aligned with the marks on the platform on the negative end
Make sure that the open end of the wells is facing upwards to receive the samples
Cover gel with 1 x TAE buffer (135 ml recommended) by filling one side of the gel tray, and watching the liquid force air out from under the gel. Then fill the other side until the gel is just covered.
Place photo hood onto unit and check green power light is solid before loading samples
Don’t forget gloves and eye protection when handling the TAE buffer

## Slide 38
Lab 5: gel loading tips …
Spread the electrophoresis tanks out as much as possible around the room before loading. Do not move once loaded
Everyone gets hand-wobble, especially when doing a new lab procedure, so support your hand or wrist to help keep steady
Try not to jab through the bottom or sides of the well, allow the dense loading dye to help the sample sink into well
When you dispense your sample into the well push to the second stop on the pipette and hold there while removing the pipette from the buffer to avoid sucking the sample back up again!
Use a new tip for each sample to avoid contamination
We are usually loading 10 ul per well

## Slide 39
Pipette tip
Well
Agarose gel
TAE buffer
Gel electrophoresis

## Slide 40
Gel electrophoresis (TT)
Xylene cyanol ~ 4,000 bp
Bromophenol blue ~ 500 bp
Orange G ~ 50 bp

## Slide 41
P is programme, use with macro mode, flash off
C is custom
No zoom improves quality
Focus before taking
Gel electrophoresis (TT)

## Slide 42
RESULTS
FROM DIGESTS AND LIGATION

## Slide 43
Plasmid Digest & Ligation
K-
K+
A-
A+
Lig
1 kb
3000 >
1000 >
500 >

## Slide 44
A+
K-
K +
A-
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
1 Kb
Lab 5: gel electrophoresis
LIG
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
A+
K-
K+
A-
1 Kb
LIG

## Slide 45
A+
K-
K +
A-
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
1 Kb
Lab 2: restriction digestion

## Slide 46
A+
K-
K +
A-
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
1 Kb
Lab 2: restriction digestion

## Slide 47
A+
K-
K +
A-
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
1 Kb
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
A+
K-
K+
A-
1 Kb
Lab 2: restriction digestion
multimer
Nicked circle
supercoiled

## Slide 48
High Resolution – Scanning Electron Microscope imaging of the three-dimensional surface topology of (a) supercoiled plasmid pUC21, (c and d) open-circular DNA molecules of pBR322 plasmid.
Taken from; YAFFEE, M, WALTER, P., RICHTER, C. and MULLER, M. (1996) Direct observation of iron-induced conformational changes of mitochondrial DNA by high-resolution field-emission in-lens scanning electron microscopy (DNA unwinding/iron colloid formation/backscattered electron detection). Proceedings of the National Academy of Sciences of the USA 93; pp. 5341-5346.
Lab 2: restriction digestion

## Slide 49
Clone that gene
Restriction enzyme | Recognition site
BamHI | GGATCC CCTAGG
EcoRI | GAATTC CTTAAG
HindIII | AAGCTT TTCGAA

## Slide 50
Objectives
By the end of this course you will:
Feel confident preparing for labs 1, 2 , 3 & 5
Feel confident carrying out labs 1, 2 , 3 & 5
Be aware of Health and Safety requirements
Know where to access resources
Know who to contact for support