## Slide 1
Biotechnology in the classroom (Course 2)
> DATE <
#biotechexperience

## Slide 2
Objectives
By the end of this course you will:
Feel confident preparing for labs 4/4a, 5, 6/6a, 7/7a
Feel confident carrying out labs 4/4a, 5, 6/6a, 7/7a
Be aware of Health and Safety requirements
Know where to access resources
Know who to contact for support

## Slide 3
Micro-pipetting
P20 – used in Y1 – max. volume 20ul
P200 – used with P20 in Y2 – for vols between 20 and 200ul

## Slide 4
Introducing PCR
1 – Who invented PCR?
2 – What are the 3 stages of PCR?
3 – How many uses of PCR can you hear?
PCR

## Slide 5
Introducing PCR

## Slide 6
Introducing PCR

## Slide 7
Number of PCR cycles | Lengths of dsDNA
1 | 2
2 | 4
5 | 32
10 | 1,024
20 | 1,048,576
35 | 34,359,738,368
Introducing PCR

## Slide 8
PCR
Detect mutations
Paternity testing
Forensic analysis
Sequencing
Phylogenetic research
Gene function
Recombination
Diagnosis of hereditary disease
Diagnosis of infectious disease
Introducing PCR

## Slide 9
Introducing PCR

## Slide 10
DNA template
Primers (forward and reverse)
Nucleosides (dATP, dCTP, dGTP, dTTP) = dNTPs
Magnesium chloride
Buffer
DNA polymerase from a thermophilic bacteria
Introducing PCR

## Slide 11
Template DNA

## Slide 12
Template DNA

## Slide 13
Template DNA

## Slide 14
PCR Set-Up
1. Using small PCR tubes, find one labelled PRI
2. Add water
3. Add MM
4. Add template DNA
6. Run thermal cycler
5. Mix with tip
DNA
MM
H2O
PRI

## Slide 15
Setting up PCRs
Reagent | NEG PCR | pARA PCR | pARA-R PCR | Ligation PCR | Colony PCR (s)
Combined primers (PRI) * | 2.0 μl | 2.0 μl | 2.0 μl | 2.0 μl | 2.0 μl
Nuclease-free water (H2O) | 10.5 μl | 8.5 μl | 8.5 μl | 5.5 μl | 9.5 μl
Master Mix (MM) | 12.5 μl | 12.5 μl | 12.5 μl | 12.5 μl | 12.5 μl
pARA plasmid (A) |  | 2.0 μl |  |  | 
pARA-R plasmid (R) |  |  | 2.0 μl |  | 
Ligation (LIG) |  |  |  | 5.0 μL | 
Colony |  |  |  |  | ~1 μl
* Combined primers are already aliquoted into mini-tubes. Total vol for all reactions, 25.0 μl

## Slide 16
Running PCRs
Reagent | Temp. (°C) | Time (sec)
Initial denaturation | 95 | 200
Denaturation 30 cycles of Annealing Extension | 95 53 68 | 30 30 30
Final extension | 68 | 300
Hold | 4 | Indefinite

## Slide 19
Assembly resource
AVAILABLE:
Introductory pictures
Assembly slides with notes
AIM:
Increase profile of Science
Introduce students to Molecular Biology
Link to ABE program in your school – increasing awareness among staff and students

## Slide 20
DNA identifies you

## Slide 21
Alec Jeffreys

## Slide 22
DNA fingerprinting
Alec Jeffreys

## Slide 23
Scene of
Crime DNA
Suspect 1
Suspect 2
Suspect 3
DNA fingerprinting

## Slide 24
DNA fingerprinting
Reuniting families

## Slide 25
DNA fingerprinting
Colin Pitchfork
1st Murder conviction

## Slide 26
Alec Jeffreys: identifying through DNA
DNA fingerprinting

## Slide 27
Your actions define you.
DNA identifies you.
DNA fingerprinting

## Slide 29
Variable Number Tandem Repeats
(VNTRs)
DNA profiling

## Slide 30
DNA profiling

## Slide 31
DNA fingerprinting in zoology: past, present, future | Investigative Genetics | Full Text (biomedcentral.com)
DNA profiling

## Slide 32
Chromosome 3 from mother
Chromosome 3 from father




DNA profiling - 1

## Slide 33
Chromosome 3 from mother
Chromosome 3 from father
DNA profiling

## Slide 34
DNA ladder
CS sample
Suspect 2
Suspect 1
Suspect 3
DNA profiling - 2

## Slide 35
DNA profiling - 3

## Slide 36
Cut the DNA either side of a VNTR region using restriction enzymes
Separate the DNA fragments containing the VNTR sequence using gel electrophoresis
Visualise the DNA using a special stain, UV transilluminator and digital camera
Identify the cake thief!
DNA profiling

## Slide 37
Restriction enzymes
3
1
2

## Slide 38
HindIII
Haemophilus influenza
BamHI
Bacillus amyloliquefaciens
Restriction enzymes

## Slide 39
Add 4 ul restriction buffer, ‘BF’ to each DNA sample. Use a new tip every time.
3. Mix each sample gently, swirling with the pipette tip.
BF
DNA profiling

## Slide 40
ENZ
Add 2 ul of restriction enzyme, ‘ENZ’ to each of the DNA samples. Use a new tip everytime and pipette into the solution at the bottom of the tube
DNA profiling

## Slide 41
DNA Fingerprinting / DNA profiling
Schootland yard
DNA profiling

## Slide 42
Schootland yard
1
2
3
4
5

## Slide 43
DNA Profiling – model gel
Ref
1 kb
DNA 1
DNA 2
DNA 3
DNA 4
DNA 5

## Slide 45
Electrophoresis prep.
400 ml 1 x TAE buffer from 50 x concentrate
8 ml of 50 x TAE buffer + 392 ml of distilled water
0.8% agarose gel, 35 ml in volume
0.28 g agarose + 35 ml 1 x TAE buffer
Remember gloves and goggles when handling TAE buffer

## Slide 46
Number of samples will dictate which comb you use
DNA Fingerprinting – Ref + 5 suspects + marker = 7
PCR of ‘rfp’ – some/all of
A-plasmid R-plasmid H2O (-ive ct) Red colony White colony
Electrophoresis prep.

## Slide 47
Agarose gel with 15 wells
10 µl DNA ladder
12.5 µl DNA1
12.5 µl DNA2
12.5 µl DNA3
12.5 µl DNA4
12.5 µl DNA5
12.5 µl CS sample
10 µl DNA ladder
12.5 µl DNA1
12.5 µl DNA2
12.5 µl DNA3
12.5 µl DNA4
12.5 µl DNA5
12.5 µl CS sample
Group 1
Group 2
Gel layout - suggestion

## Slide 48
Pipette tip
Well
Agarose gel
SB buffer
Gel electrophoresis

## Slide 49
Gel electrophoresis

## Slide 50
Lab 5: gel electrophoresis
Xylene cyanol ~ 4,000 bp
Bromophenol blue ~ 500 bp
Orange G ~ 50 bp

## Slide 51
Lab 9: DNA profiling
CS / DNA Ref
1 kb marker
DNA 1
DNA 2
DNA 3
DNA 4
DNA 5
So who dunnit?

## Slide 52
Electrophoresis – 2 ways
Tanks & transilluminator (TT)
Mini-One (MO)
Electrical Hazards – clear up spills immediately. Keep power packs raised above lab bench surface

## Slide 53
Lab 5: gel tank assembly

## Slide 54
Lab 5: Mini-One assembly

## Slide 55
Electrophoresis – 2 ways
Tanks & transilluminator (TT)
Mini-One (MO)
0.8% gel, 1 x TAE buffer
30-35 ml agarose for each gel
200-300 ml buffer needed
8 or 15 teeth (samples) per gel
Add LD to samples
LD – regular
Load / black card below tank
Run time: 30-45 min
Post-stain: 30 min / Gel Red
Download gel images and share results
0.8% gel, 1 x TAE buffer
11 ml agarose for each gel
135 ml buffer needed
6 or 9 teeth (samples) per gel
Add LD to samples
Ensure LD contains Gel Green
Load under blue light
Run ‘live’ : 20-30 min
No post-stain required
Result recorded directly by students on smartphone

## Slide 56
Current DNA Stains
Gel Red (used in TT)
Gel Green (used in MO)
GelRed® is an ultra sensitive, extremely stable and environmentally safe fluorescent nucleic acid dye designed to replace the highly toxic ethidium bromide (EtBr) for staining dsDNA, ssDNA or RNA in agarose gels or polyacrylamide gels.
Safer than EtBr: non-mutagenic and non-hazardous for disposal
Much more sensitive than EtBr and SYBR® Safe
Stable at room temperature and microwavable
Simple precast or post-electrophoresis gel staining, no destaining
GelGreen® is a highly sensitive, stable and environmentally safe, green fluorescent nucleic acid stain • Non-mutagenic - at concentrations relevant to nucleic acid gel staining • Non-cytotoxic - at concentrations relevant to nucleic acid gel staining • Cell membrane impermeability for true safety • Impenetrable to latex gloves • Very photostable - use under normal room light • Hydrolytically stable • Microwaveable
Remember gloves and goggles when using the stains

## Slide 57
Current DNA Stains
Gel Red (used in TT)
Gel Green (used in MO)
Image c/o VWR - https://uk.vwr.com/store/product/826590/gelredtm-and-gelgreentm-nucleic-acid-gel-stains

## Slide 58
Before Loading
Remove the masking tape from the ends of your gel tray
Place the gel, and its casting tray, into the electrophoresis tank. The wells should be at the black (negative end), as DNA is negatively charged and will run towards the red (positive) end.
Make sure that the open end of the wells is facing upwards to receive the samples
Submerge the gel in 1X TAE buffer (this contains the ions needed for electrophoresis). There needs to be 1-2 mm of buffer over the top of the gel. Too much and the current will go through the buffer and not the gel! Pour buffer onto the gel until just after the well dimples disappear.
Remove the comb from your agarose gel by lifting it directly upwards. The comb will create some suction, so it needs a gentle, but consistent upwards pressure.
Place a black sheet under the wells to make them more visible
Remove the comb from your agarose gel by lifting it directly upwards.
Place the gel, and its casting tray into the electrophoresis tank (only fits one way!). Remember the black supporting platform and make sure the wells are aligned with the marks on the platform on the negative end
Make sure that the open end of the wells is facing upwards to receive the samples
Cover gel with 1 x TAE buffer (135 ml recommended) by filling one side of the gel tray and watching the liquid force air out from under the gel. Then fill the other side until the gel is just covered.
Place photo hood onto unit and check green power light is solid before loading samples
Don’t forget gloves and eye protection when handling the TAE buffer

## Slide 59
PCRs onto Gel
Reagent | NEG gel | A gel | R gel | LIG gel | C gel
Loading Dye | 2.0 μL | 2.0 μL | 2.0 μL | 2.0 μL | 2.0 μL
Nuclease-free water (H2O) | 6.0 μL | 6.0 μL | 6.0 μL | 6.0 μL | 6.0 μL
Neg PCR (water only) | 2.0 μL |  |  |  | 
pARA plasmid (A) - PCR |  | 2.0 μL |  |  | 
pARA-R plasmid (R) - PCR |  |  | 2.0 μL |  | 
Ligation (LIG) - PCR |  |  |  | 2.0 μL | 
Colony PCR |  |  |  |  | 2.0 μL
Each PCR sample, needs to be prepared for loading onto gel – either a MiniOne gel or the traditional format. Add 4μl loading dye DIRECT TO PCR samples, mix, and LOAD into 10μl into gel

## Slide 60
Biotechnology for the classroom
Bacterial Transformation

## Slide 61
Horizontal Gene Transfer
Horizontal gene transfer (HGT) is the movement of genetic information between organisms, a process that includes the spread of antibiotic resistance genes among bacteria

## Slide 62
Conjugation Transduction Transformation
Horizontal Gene Transfer

## Slide 63
Lab 6a: transformation
Recombinant Plasmids
Competent Cells
pARA-R

## Slide 64
Lipid bilayer
(inner)
Lipid bilayer
(outer)
Peptidoglycan
layer
Adhesion zone
Calcium ions
Lab 6a: transformation

## Slide 65
Calcium ions
pARA-R
Adhesion zone
Lipid bilayer
(inner)
Lipid bilayer
(outer)
Peptidoglycan
layer
Lab 6a: transformation

## Slide 66
Transformation Theory
Lab 6a: transformation
Lab 6a: transformation

## Slide 67
Keep cells cold
Heat shock at exactly 42C
Spread don’t gauge agar
Lab 6a: transformation

## Slide 68
Follow good aseptic technique. Gloves do not need to be worn. All tips & tubes into Virkon (or equivalent)
Lab 6a: transformation

## Slide 70
P- plates
LB
LB/amp
No growth
P+ plates
LB
LB/amp
LB/amp/ara
Lab 6a: transformation

## Slide 71
Taken from; YAFFEE, M, WALTER, P., RICHTER, C. and MULLER, M. (1996) PNAS of the USA 93; pp. 5341-5346.
LB/amp/ara
Supercoiled plasmid
Relaxed circle plasmid
Lab 6a: transformation

## Slide 72
colony
satellite colonies
Lab 6a: transformation

## Slide 73
Colony isolation and culture
LB/amp/ara
broth
Lab 6a: transformation

## Slide 74
Lab 6a: transformation

## Slide 75
Overnight
culture
Cell pellet
with RFP
Lysed
cells
Pellet
cell debris
RFP with
binding buffer
Lab 6a: transformation

## Slide 76
Lab 6a: transformation

## Slide 77
Making protein therapeutics
chromosome
E. coli
plasmids
plasmid

digest plasmid
gene of interest
recombinant plasmid
protein produced
E. coli with recomb-inant plasmid
protein purified

## Slide 78
Objectives
By the end of this course you will:
Feel confident preparing for labs 4/4a, 5, 6/6a, 7/7a
Feel confident carrying out labs 4/4a, 5, 6/6a, 7/7a
Be aware of Health and Safety requirements
Know where to access resources
Know who to contact for support

## Slide 80
ONLINE FOLLOW-UP - RESULTS
Lab 6/6a ’

## Slide 81
Lab 4/7 – Finding ‘rfp’
1 kb
Red
White
Ligation
R-plasmid
A-plasmid
Water

## Slide 82
1 Kb
1 Kb
1 Kb
R -
R +
MMpARA-R
MMRed
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
PCR: lab 4a

## Slide 83
1 Kb
1 Kb
1 Kb
R -
R +
MMpARA-R
MMRed
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
PCR: lab 7a

## Slide 84
1 Kb
1 Kb
1 Kb
R -
R +
MMpARA-R
MMRed
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
1 Kb
1 Kb
1 Kb
R -
R +
MMpARA-R
MMRed
PCR: lab 4a and 7a

## Slide 85
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
A+
K-
K +
A-
MMpARA
Ligation
1 Kb
MMLIG
MMpARA-R
1 Kb
PCR: lab 4

## Slide 86
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
A+
K-
K +
A-
MMpARA
Ligation
1 Kb
MMLIG
MMpARA-R
1 Kb
PCR: lab 4

## Slide 87
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
A+
K-
K +
A-
MMpARA
Ligation
1 Kb
MMLIG
MMpARA-R
1 Kb
pARA PCR
Ligation reaction
Ligation PCR
pARA-R PCR
PCR: lab 4

## Slide 88
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
A+
K-
K +
A-
MMpARA
Ligation
1 Kb
MMLIG
MMpARA-R
1 Kb
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
A+
K-
K +
A-
MMpARA
Ligation
1 Kb
MMLIG
MMpARA-R
1 Kb
PCR: lab 4

## Slide 89
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
A+
K-
K +
A-
MMpARA
Ligation
1 Kb
MMLIG
MMpARA-R
1 Kb
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
A+
K-
K +
A-
MMpARA
Ligation
1 Kb
MMLIG
MMpARA-R
1 Kb
PCR: lab 4

## Slide 90
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
1 Kb
1 Kb
MMpARA-R
MMRed
MMWhite
MMWhite
MMWhite
pARA-R PCR
PCR: lab 7

## Slide 91
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
1 Kb
1 Kb
MMpARA-R
MMRed
MMWhite
MMWhite
MMWhite
LB/amp/ara
primer
primer
1092 bp PCR fragment
primer
primer
662 bp PCR fragment
PCR: lab 7

## Slide 92
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
1 Kb
1 Kb
MMpARA-R
MMRed
MMWhite
MMWhite
MMWhite
LB/amp
primer
primer
1092 bp PCR fragment
primer
primer
662 bp PCR fragment
PCR: lab 7

## Slide 93
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
1 Kb
1 Kb
MMpARA-R
MMRed
MMWhite
MMWhite
MMWhite
10.0
0.5
1.0
1.5
2.0
3.0
4.0
6.0
8.0
5.0
1 Kb
1 Kb
MMpARA-R
MMRed
MMWhite
MMWhite
MMWhite
PCR: lab 7

## Slide 94
Plasmids from ligation

## Slide 95
Plasmids in white colonies
662 bp fragment by PCR
136 bp from BamHI site
149 bp from HindIII site
377 bp restriction fragment
4780 bp fragment by PCR
136 bp from BamHI site
149 bp from HindIII site
4495 bp restriction fragment
4990 bp fragment by PCR
136 bp from BamHI site
149 bp from HindIII site
4705 bp restriction fragment

## Slide 96
Thank you !